## Slide 1: Docker 101

## Slide 2: What is Docker?
Docker is a containerization technology that enables lightweight application segmentation, portability and isolation
  Functionally similar to, but much lighter weight than, traditional Virtual Machines (VMs)
  Four to six times more containerized applications can be run on a given server machine than the if the applications were to be run in separate VMs (when done properly)
  Docker lends itself to Continuous Integration/Continuous Deployment (CI/CD) build, test and deployment environments
  Used heavily in cloud-scale application development

## Slide 3: How does Docker differ from traditional VMs?
VMs use hardware virtualization and hypervisors, and can run different operating systems and kernels on separate VMs on the same hardware
Docker uses OS virtualization, the host kernel is shared among all containers
VMs running on the same host may be more secure than containers, but when developing or running trusted containers, this is often not a primary concern
Containers boot much faster than VMs (milliseconds vs. seconds), which makes scaling applications up and down much simpler

## Slide 4: VMs vs. Containers

## Slide 5: Benefits of Containers
Reduced IT management resources
Reduced size of snapshots vs. VM images
Quicker spinning up apps – milliseconds vs. seconds or minutes
Reduced & simplified security updates
Less code to transfer, migrate, upload workloads
Isolated application environment
Complex environments are easily shared, when built properly e.g. without external dependencies. Solves the ‘works on my machine’ problem
Greatly improved repeatability for application build and deploy

## Slide 6: What Docker can help with at SSCI
Containerizing complex build environments can eliminate the dependency on a single, hard to maintain build machine
Containers can make it easy to have multiple, different test environments that can be layered on top of a common substrate
Docker container layers can help abstract common environments, allowing developers to focus on any additional configuration or tooling needed to, for example, build multiple versions of a system as requirements change over time.

## Slide 7: Getting started with Docker
https://phoenixnap.com/kb/how-to-install-docker-on-ubuntu-18-04
docker run hello-world
docker pull python
docker image ls
docker ps [-a]
docker history python:latest
docker system prune -a

## Slide 8: Example Python application (Python 3.6+)
import platform
print(f'Hi from Python {platform.python_version()}')

## Slide 9: Example Dockerfile
FROM python:latest
COPY hi.py .
CMD python hi.py

## Slide 10: Building and running a Docker image
docker build . --tag hi:latest

## Slide 11: Mounting host paths into a container

## Slide 12: Use cases

## Slide 13: Reference and Further Reading
https://docs.docker.com/samples/
https://docs.docker.com/develop/develop-images/dockerfile_best-practices/
https://cloud.google.com/blog/products/gcp/7-best-practices-for-building-containers

## Slide 14: Useful docker commands
Save a container to a .tar or .tar.gz:
  docker save myimage:latest > myimage_latest.tar
  docker save myimage:latest | gzip > myimage_latest.tar.gz